BOEING 737-800 NORMAL CHECKLIST

PRE FLIGHT CHECKLIST
PARKING BRAKE SET / BATTERY GUARD CLOSED / STANDBY POWER GUARD CLOSED / GND PWR AVAIL GND PWR SWITCH ON / LIGHTS TEST PERFORMED / OXYGEN & MASK CHECKED / FIRE WARN TEST PERFORMED / APU START / APU GEN ON / POSITION LIGHTS STEADY / LOGO LIGHT AS REQUIRED / EMER EXIT LIGHTS GUARD CLOSED / PASSENGER SIGNS ON / PACKS AUTO/HIGH / ISOLATION VALVE OPEN / ENG / APU BLEED ON / IRS MODE SELECTORS OFF>NAV / FMC SET / Request Flight-Plan Clearance / TRANSPONDER SET / MCP V2 SET / MCP HDG / TAKEOFF RWY SET / MCP INITIAL ALT SET / YAW DAMPER ON / WINDOW HEAT ON / FLIGHT ALTITUDE SET / LANDING ALTITUDE SET / FLIGHT DIRECTORS ON / LNAV AS REQUIRED / VNAV AS REQUIRED / MINIMUMS REF BARO or RADIO / MINIMUMS SET / ALTIMETER REF IN or HPA / ALTIMETER SET / AUTO BRAKE RTO / COM RADIOS SET / DOORS CLOSED

BEFORE START CHECKLIST
Request Pushback & Startup Clearance / AUTOPILOT DISENGAGE BAR UP / AUTOTHROTTLE ARM / FUEL PUMPS ON / HYDRAULIC PUMPS ON / ANTI COLLISION LIGHT ON / GROUND EQUIPMENT REMOVED / ENGINE AREA CLEAR

ENGINE START CHECKLIST
ENGINE DISPLAY SELECT / PACKS OFF / ENGINE START SWITCH GND / ENGINE START LEVER IDLE AT 25% N2

BEFORE TAXI CHECLIST
GENERATORS 1 & 2 ON / PROBE HEAT ON / WING ANTI ICE AS REQUIRED / ENGINE ANTI ICE AS REQUIRED / PACKS AUTO / ISOLATION VALVE AUTO / APU BLEED OFF / APU OFF / ENGINE START SWITCHES CONT / FLAPS SET FOR T/O / ELEVATOR TRIM SET FOR T/O / FLIGHT CONTROLS CHECK / RECALL CHECK / Request Taxi Clearance / TAXI LIGHTS ON / RWY TURNOFF LIGHTS AS REQUIRED

BEFORE TAKE-OFF CHECKLIST
FUEL FLOW RESET, then RATE / CENTER FUEL PUMPS AS REQUIRED / ANTI-ICE AS REQUIRED / FLIGHT INSTRUMENTS CHECK / ENGINE INSTRUMENTS CHECK / TAKE-OFF DATA (V1,VR,V2) CHECK / Request Take-Off Clearance / LANDING LIGHTS ON / STROBE LIGHT ON / TAXI LIGHTS OFF / TRANSPONDER TA/RA / TFC PUSH ON / CLOCK START

AFTER TAKE-OFF CHECKLIST
POSITIVE RATE OF CLIMB GEAR UP / AUTO-BRAKE OFF / ENGINE START SWITCHES OFF / GEAR LEVER OFF / RWY TURN-OFF LIGHTS OFF

CLIMB AND CRUISE CHECKLIST
CMD A or B ENGAGE / Passing Transition Altitude / ALTIMETER SET STD / BELOW 10'000FT MAX 250 KIAS / Passing 10'000 FT / LANDING LIGHTS OFF / FASTEN SEAT BELTS OFF / CENTER FUEL PUMPS AS REQUIRED / Cruise / ENGINE & INSTRUMENTS MONITOR / FUEL QUANTITY CHECK

DESCENT CHECKLIST
Before Top Of Descent / ATIS / AIRPORT INFO CHECK / ALTIMETER CHECK / RADIOS SET / RESET MCP ALTITUDE CHECK / VREF SET / LOCALIZER FREQ SET / IS LOC COURSE SET / Descent / ANTI-ICE AS REQUIRED / LANDING ALTITUDE CHECK / RECALL CHECK / RADIO ALT / BARO MIN SET / AUTO BRAKE AS REQUIRED / Passing Transition Altitude / ALTIMETER RESET TO LOCAL / Below 10'000 FT / SPEED MAX 250 KIAS / LANDING LIGHTS ON / PASSENGER SIGNS ON

APPROACH CHECKLIST
ALTIMETER CHECK / LOCALIZER FREQUENCY CHECK / LOCALIZER COURSE CHECK / APP ARM / GLIDESLOPE ALIVE GEAR DOWN / FLAPS 15 / SPEED BRAKE ARM / 2ND AUTOPILOT ARM / ENGINE START SWITCHES CONT / LANDING FLAPS SET

LANDING CHECKLIST
GO-AROUND ALTITUDE SET / RWY TURN-OFF LIGHTS ON / LANDING GEAR CHECK DOWN / AUTOPILOT AS REQUIRED / AUTO-THRUST AS REQUIRED

LANDING ROLL CHECKLIST
THRUST REVERSE ENGAGE / AUTOPILOT OFF / AUTOTHRUST OFF / AT 60 KTS REV THRUST TO IDLE / AT 30 KTS AUTO-BRAKE DISENGAGE

AFTER LANDING CHECKLIST
TRANSPONDER AS REQUIRED / FLAPS RETRACT / SPEED BRAKE DOWN / LANDING LIGHTS OFF / POSITION LIGHTS STEADY / TAXI LIGHTS ON / ANTI ICE AS REQUIRED / APU START / PROBE HEAT OFF / ENGINE START SWITCHES OFF / AUTO-BRAKE OFF / Taxi To Gate / RWY TURNOFF LIGHTS OFF / APU GEN ON / TAXI LIGHTS OFF

PARKING / SHUTDOWN CHECKLIST
PARKING BRAKES SET / ENGINE START LEVERS CUTOFF / GROUND OPERATIONS AS REQUIRED / PASSENGER SIGNS OFF / APU BLEED AIR ON / ANTI COLLISION LIGHT OFF / FUEL PUMPS OFF / ANTI-ICE OFF / HYDRAULIC PUMPS OFF / ISOLATION VALVE OPEN / FLIGHT DIRECTOR OFF / GND POWER ESTABLISH / DOORS OPEN

SECURING AIRCRAFT
IRS MODE SELECTORS OFF / APU OFF / EMERGENCY EXIT LIGHTS OFF / WINDOW HEAT OFF / PACKS OFF / STANDBY POWER OFF / BATTERY OFF

AIRPORT BAR CHECKLIST
ORDER DRINK CHECK